## Slide 1: Introduction to STM32 Microcontroller

## Slide 2: Rundown
GPIO with blinking LED example
Timer and PWM with ultrasonic sensor example
UART sending and receiving in interrupt mode

## Slide 3: Workflow for STM32
STM32CubeIDE
STM32CubeProgrammer
Notes: The first step in the process is to create the source code, then using a cross compiler to generated binary code that will run on the stm32
Then the linker will link all necessary binary libraries to form a fully executable MCU program
The generated binary code will be load on the STM32 by the cubeprogrammer

## Slide 4: GPIO

## Slide 5: Step 1: Create New Project
Launch STM32CubeIDE
The Project will be saved in the directory of the workspace

## Slide 7
In the Part Number Type:
  STM32F051R8
Then select Package LQFP64
Click next

## Slide 9: Step 2: GPIO Pin Configuration
Click PC8 and select GPIO_Output
Click PA0 and select GPIO_Input

## Slide 10
In System Core -> GPIO select PA0
  In the User Label box type in BUTTON
  For PC8, type in LED
Save the STM32CubeMX settings by Ctrl + S, and then select YES to start generating source code.

## Slide 11: Step 3: User code
Insert the following code in the while loop under main()
Build the application by pressing Ctrl + B, or in menu Project → Build All
int main(void) {
while (1) {
if (HAL_GPIO_ReadPin(BUTTON_GPIO_Port, BUTTON_Pin) == GPIO_PIN_SET) {
HAL_GPIO_WritePin(LED_GPIO_Port, LED_Pin, GPIO_PIN_SET);
HAL_Delay(100);
HAL_GPIO_WritePin(LED_GPIO_Port, LED_Pin, GPIO_PIN_RESET);
HAL_Delay(100);
} else {
HAL_GPIO_WritePin(LED_GPIO_Port, LED_Pin, GPIO_PIN_SET);
HAL_Delay(500);
HAL_GPIO_WritePin(LED_GPIO_Port, LED_Pin, GPIO_PIN_RESET);
HAL_Delay(500);
}
}
}

## Slide 12: Step 4 : Download to the board
Launch STM32CubeProgrammer
Select ST_LINK
Click Connect

## Slide 13
Click the download icon at the right
Browse for the project name.bin in the Debug file under workspace/project name
Click Start Programming

## Slide 14: Interrupt
Change Pin PA0 configuration from GPIO_Input to GPIO_EXTI0
In System Core -> NVIC
  Enable EXTI line 0 and 1 interrupt

## Slide 15: Handle interrupt
In main.c insert the code and remove the code in previous steps
Rebuild and download the application to the board
void HAL_GPIO_EXTI_Callback(uint16_t GPIO_Pin) {
HAL_GPIO_TogglePin(LED_GPIO_Port, LED_Pin);
}

## Slide 16: Timer and PWM

## Slide 17: Basic overview
Pre-scaler and counter period
  Pre-scaler is used to reduce the counting speed
  Counter period determined how many tick until the counter overflow
Example:
  Fsys = 48 MHz
  Pre-scaler = 1024
  Timer gets incremented by 1 every 1024* 1/48000000 s = 21.3 us
  If set overflow at full 16-bit (at 65535), and start counting from 0, it will generate a signal every 21.3 us * 65535 = 1395896 us = 1395.896 ms

## Slide 18: System clock configuration
Set the HCLK to 48 MHz

## Slide 19: Blinking LED with timer
Enable TIM6 (basic timer)
Set the pre-scaler to 2999 (3000 – 1)
Set the counter period to 3999 (4000 – 1)

## Slide 20: Enable timer interrupt
Enable interrupts in NVIC settings

## Slide 21: User code
Start the timer in interrupt mode
Override the callback function when a full period elapses
int main() {
...
HAL_TIM_Base_Start_IT(&htim6);
while (1){...}
}
void HAL_TIM_PeriodElapsedCallback(TIM_HandleTypeDef *htim) {
HAL_GPIO_TogglePin(LED_GPIO_Port, LED_Pin);
}

## Slide 22: Setup PWM on a Timer
Enable TIM1 and configure Clock Source as Internal Clock
Configure Channel 1 as PWM Generation CH1
Pre-scaler = 480, Counter Period = 1000 -> PWM frequency = 100Hz
PWM Pulse = 250 -> duty cycle = 250/1000 = 25%

## Slide 23: User code
Enable the PWM generation as the configuration
int main() {
...
HAL_TIM_PWM_Start(&htim3, TIM_CHANNEL_3);
while (1){...}
}

## Slide 24: Setup Timer for Input Capture
Change TIM1 Channel 1 to Input Capture direct mode
Configure Pre-scaler to 48 – 1 and Counter Period to 0xffff – 1

## Slide 25: User code for ultrasonic sensor
Enable Input Capture interrupt
Create a function for delay in us
Create a function for sending trigger pulse to the ultrasonic sensor
Override the interrupt callback function
void delay (uint16_t time)
{
__HAL_TIM_SET_COUNTER(&htim1, 0);
while (__HAL_TIM_GET_COUNTER (&htim1) < time);
}
void Ultrasonic_Read()
{
HAL_GPIO_WritePin(US_TRIG_GPIO_Port, US_TRIG_Pin, GPIO_PIN_SET);
delay(10);
HAL_GPIO_WritePin(US_TRIG_GPIO_Port, US_TRIG_Pin, GPIO_PIN_RESET);
__HAL_TIM_ENABLE_IT(&htim1, TIM_IT_CC1);
}
int main() {
...
HAL_TIM_IC_Start_IT(&htim1, TIM_CHANNEL_1);
while (1){...}
}

## Slide 26
void HAL_TIM_IC_CaptureCallback(TIM_HandleTypeDef *htim)
{
if((htim->Instance == TIM1) && (htim-> Channel == HAL_TIM_ACTIVE_CHANNEL_1)) // if the interrupt source is channel1
{
if (!Is_First_Captured) // if the first value is not captured
{
First_Val = HAL_TIM_ReadCapturedValue(htim, TIM_CHANNEL_1); // read the first value
// Now change the polarity to falling edge
__HAL_TIM_SET_CAPTUREPOLARITY(htim, TIM_CHANNEL_1, TIM_INPUTCHANNELPOLARITY_FALLING);
Is_First_Captured = 1; // set the first captured as true
}
else
{
Sec_Val = HAL_TIM_ReadCapturedValue(htim, TIM_CHANNEL_1); // read second value
__HAL_TIM_SET_COUNTER(htim, 0); // reset the counter
if (Sec_Val > First_Val)
{
Difference = Sec_Val-First_Val;
}
else if (First_Val > Sec_Val)
{
Difference = (0xffff - First_Val) + Sec_Val;
}
Distance = Difference * .034/2;
// set polarity to rising edge
__HAL_TIM_SET_CAPTUREPOLARITY(htim, TIM_CHANNEL_1, TIM_INPUTCHANNELPOLARITY_RISING);
__HAL_TIM_DISABLE_IT(&htim1, TIM_IT_CC1);
Is_First_Captured = 0; // set it back to false
}
}
}

## Slide 27: UART

## Slide 28: Setup UART
Enable USART1 and set the Baud Rate to 9600

## Slide 29
Enable interrupt in NVIC Settings

## Slide 30
Enable float formatting in setting by right click the project-> Properties -> C/C++ Build -> Settings -> MCU settings -> check Use float with printf…

## Slide 31: Send data with interrupt
Use HAL_UART_Transmit_IT() function to send data.
char counter = 0;
char buffer[16] = { 0 };
int main() {
char pause = 0;
while(1) {
if (pause == 0) {
sprintf(buffer, "counter=%03d\n\r", counter++);
HAL_UART_Transmit_IT(&huart1, (uint8_t*) buffer, strlen(buffer));
}
HAL_Delay(1000);
}
}

## Slide 32: Receive data with interrupt
Use HAL_UART_Receive_IT() to read data
Interrupt will issue when the receiver get enough byte and run HAL_UART_RxCpltCallback() function
char counter = 0;
char buffer[16] = { 0 };
Char rx_buffer[16] = {0};
void HAL_UART_RxCpltCallback(UART_HandleTypeDef *huart) {
if (huart == &huart1) { uart_rx_int = 1; }
}
int main() {
char pause = 0;
while(1) {
if (pause == 0) {
sprintf(buffer, "counter=%03d\n\r", counter++);
HAL_UART_Transmit_IT(&huart1, (uint8_t*) buffer, strlen(buffer));
}
if (uart_rx_int == 1) {
uart_rx_int = 0;
if (strncmp(command, "stop", 4) == 0)
{
pause = 1;
} else if (strncmp(command, "resume", 6) == 0)
{
pause = 0;
}
}
HAL_UART_Receive_IT(&huart1, (uint8_t*) buffer, n);
HAL_Delay(1000);
}
}

## Slide 33: Challenge

## Slide 34: Try using UART to send the reading from the ultrasonic sensor